## Slide 1
氨基酸手性分析：有文献依据的方法—试剂对应
分析方法
衍生化试剂／直接分析
HPLC / UPLC
高效液相色谱
异硫氰酸酯类
FITC [01]
GITC [02]
芳香亲核取代类
FDAA [02,03]
FDLA [04]
NBD-F [05]
OPA 类
OPA＋NAC / IBLC
OPA＋DiCys
[02,06,07]
磺酰氯类
Dansyl-Cl [08]
Dabsyl-Cl [09]
氨基酰化类
FMOC-Cl [10]
AQC [11]
GC
气相色谱
氯甲酸酯类
氯甲酸甲酯 [12]
五氟丙基氯甲酸酯 [13]
七氟丁基氯甲酸酯 [14]
氯甲酸酯＋手性醇
氯甲酸乙酯
＋(S)-(+)-3-甲基-2-丁醇 [15]
CE
毛细管电泳 （CZE / MEKC）
异硫氰酸酯类
FITC [16]
(R)-NCS [17]
芳香亲核取代类
NBD-F [18]
DTAF [19]
芳香二醛类
OPA＋ME [20]
OPA＋手性硫醇 [21]
NDA [22]
磺酰氯类
Dansyl-Cl [16]
氨基酰化类
FMOC-Cl [23]
FLEC [24]
HPLC–CD
液相色谱–圆二色检测
异硫氰酸酯类
PITC–PTH [25]
芳香亲核取代类
NBD-F [26]
无需衍生化
Trp [27] · Phe [28]
直接分析：Trp采用手性柱[27]；Phe采用非手性柱[28]。适用性须逐个氨基酸验证。
①手性固定相 ②手性衍生化
UV · 荧光 · MS/MS
①手性固定相 ②手性衍生化
FID · MS
①手性选择剂 ②手性衍生化
UV · 荧光 · MS
①手性固定相 ②非手性分离
CD · UV · MS
Notes: 独立文献核查版。第1页为主图，方块后的编号与配套文献表一致。不是全部试剂或全部氨基酸的兼容性清单。真实蛋白/肽水解液、游离氨基酸实样和标准品研究分别在配套报告标明。CD中AQC、OPA、PTC不保留。GC中的硅烷化及酸酐酯化未放入主图，见限制性文献29、30。HPLC-CD是HPLC的联用子类，单列仅为突出研究路线。
HPLC/UHPLC｜异硫氰酸酯类｜FITC → [01]
HPLC/UHPLC｜异硫氰酸酯类｜GITC → [02]
HPLC/UHPLC｜芳香亲核取代类｜FDAA → [02],[03]
HPLC/UHPLC｜芳香亲核取代类｜FDLA → [04]
HPLC/UHPLC｜芳香亲核取代类｜NBD-F → [05]
HPLC/UHPLC｜OPA类｜OPA＋NAC → [06]
HPLC/UHPLC｜OPA类｜OPA＋IBLC → [02],[06]
HPLC/UHPLC｜OPA类｜OPA＋DiCys → [07]
HPLC/UHPLC｜磺酰氯类｜Dansyl-Cl → [08]
HPLC/UHPLC｜磺酰氯类｜Dabsyl-Cl → [09]
HPLC/UHPLC｜氨基酰化类｜FMOC-Cl → [10]
HPLC/UHPLC｜氨基酰化类｜AQC → [11]
GC｜氯甲酸酯类｜氯甲酸甲酯（MCF） → [12]
GC｜氯甲酸酯类｜五氟丙基氯甲酸酯（PFPCF） → [13]
GC｜氯甲酸酯类｜七氟丁基氯甲酸酯（HFBCF） → [14]
GC｜氯甲酸酯＋手性醇组合｜氯甲酸乙酯＋(S)-(+)-3-甲基-2-丁醇 → [15]
CE｜异硫氰酸酯类｜FITC → [16]
CE｜异硫氰酸酯类｜(R)-NCS → [17]
CE｜芳香亲核取代类｜NBD-F → [18]
CE｜芳香亲核取代类｜DTAF → [19]
CE｜芳香二醛类｜OPA＋2-巯基乙醇（ME） → [20]
CE｜芳香二醛类｜OPA＋手性硫醇 → [21]
CE｜芳香二醛类｜NDA → [22]
CE｜磺酰氯类｜Dansyl-Cl → [16]
CE｜氨基酰化类｜FMOC-Cl → [23]
CE｜氨基酰化类｜FLEC → [24]
HPLC–CD｜异硫氰酸酯/后续转化路线｜PITC–PTH → [25]
HPLC–CD｜芳香亲核取代类｜NBD-F → [26]
[01] Chiral nano-liquid chromatography-mass spectrometry applied to amino acids analysis for orange juice profiling. (2008). DOI 10.1016/j.foodchem.2007.11.062. HPLC：FITC标记后在万古霉素手性固定相上进行nano-LC–MS分析。 核查层级：公开摘要与书目。证据位置：摘要：FITC、vancomycin-modified silica-diol、orange juice段。
[02] Chirality determination of unusual amino acids using precolumn derivatization and liquid chromatography-electrospray ionization mass spectrometry. (2004). DOI 10.1016/j.chroma.2004.02.068. HPLC：直接比较FDAA、GITC、S-NIFE及OPA–IBLC；经反相HPLC–UV/ESI-MS分析非常见氨基酸立体异构体。 核查层级：公开摘要与书目。证据位置：摘要首句四种试剂及RP-HPLC/UV/MS段。
[03] LC-MS/MS-Based Separation and Quantification of Marfey's Reagent Derivatized Proteinogenic Amino Acid DL-Stereoisomers. (2019). DOI 10.1007/s13361-018-2093-9. HPLC：FDAA/Marfey衍生化结合反相LC–MS/MS，实现19对常见手性氨基酸的分离定量。 核查层级：公开摘要与书目。证据位置：摘要：Marfey derivatization、19 pairs、MRSA extracts段。
[04] Reliable and sensitive analysis of amino acids in the peptidoglycan of actinomycetes using the advanced Marfey's method. (2007). DOI 10.1016/j.mimet.2007.05.003. HPLC：L-/D-FDLA advanced Marfey法，结合LC/MS确定细胞壁氨基酸构型。 核查层级：公开摘要与书目。证据位置：摘要：L-FDLA/D-FDLA、acid hydrolysis、cell wall段。
[05] Simultaneous determination of hydrophilic amino acid enantiomers in mammalian tissues and physiological fluids applying a fully automated micro-two-dimensional high-performance liquid chromatographic concept. (2010). DOI 10.1016/j.chroma.2009.09.002. HPLC：NBD-F标记后，反相一维分离组分，Pirkle型手性二维拆分对映体。 核查层级：公开摘要与书目。证据位置：摘要：NBD-F、Pirkle type enantioselective column、rat plasma/urine段。
[06] High-performance liquid chromatography evaluation of the enantiomeric purity of amino acids by means of automated precolumn derivatization with ortho-phthalaldehyde and chiral thiols. (2016). DOI 10.1002/chir.22660. HPLC：OPA＋NAC或IBLC自动柱前衍生化，普通PFP柱分离非对映衍生物并评价对映体杂质。 核查层级：公开摘要与书目。证据位置：摘要：N-acetyl-L-cysteine、N-isobutyryl-L-cysteine、PFP column段。
[07] Dimethylcysteine (DiCys)/o-Phthalaldehyde Derivatization for Chiral Metabolite Analyses: Cross-Comparison of Six Chiral Thiols. (2021). DOI 10.3390/molecules26247416. HPLC：OPA＋DiCys与其他五种手性硫醇比较；LC-MS分析氨基酸对映体。 核查层级：公开摘要与书目。证据位置：摘要：DiCys/OPA、six chiral thiols、rice extracts段。
[08] Enantioseparation of dansyl amino acids by HPLC on a monolithic column dynamically coated with a vancomycin derivative. (2010). DOI 10.1002/bmc.1430. HPLC：Dansyl氨基酸在万古霉素衍生物动态涂覆的整体柱上实现对映体分离。 核查层级：公开摘要与书目。证据位置：摘要：Dansyl amino acids、All investigated compounds were separated段。
[09] Simultaneous analysis of D- and L-serine in cerebrospinal fluid by use of HPLC. (2007). DOI 10.1373/clinchem.2007.086702. HPLC：Dabsyl-serine经预分离、脱盐，再在Sumichiral柱上拆分D/L并以UV–Vis检测。 核查层级：公开摘要与书目。证据位置：摘要Methods、Results及Conclusion。
[10] Imaging Peptide and Protein Chirality via Amino Acid Analysis by Chiral × Chiral Two-Dimensional Correlation Liquid Chromatography. (2018). DOI 10.1021/acs.analchem.8b00676. HPLC：FMOC氨基酸经奎宁/奎尼丁两维手性色谱分析，给出肽水解物组成与构型图。 核查层级：公开摘要与书目。证据位置：摘要：FMOC-derivatized…peptide hydrolysates；gramicidin and bacitracin段。
[11] Comprehensive Online Reversed-Phase × Chiral Two-Dimensional Liquid Chromatography-Mass Spectrometry with Data-Independent Sequential Window Acquisition of All Theoretical Fragment-Ion Spectra-Acquisition for Untargeted Enantioselective Amino Acid Analysis. (2022). DOI 10.1021/acs.analchem.2c03042. HPLC：AQC标记结合反相×手性二维LC–MS/MS，用于治疗肽水解液的组成和构型指认。 核查层级：公开摘要与书目。证据位置：摘要：AQC、chiral tandem column、two peptide hydrolysate samples及oxytocin段。
[12] Gas chromatography-mass spectrometry analysis of amino acid enantiomers as methyl chloroformate derivatives: application to space analysis. (2007). DOI 10.1016/j.chroma.2006.12.033. GC：氯甲酸甲酯/醇/吡啶衍生化，结合Chirasil-L-Val及SIM-MS，实现多对氨基酸对映体分析。 核查层级：公开摘要与书目。证据位置：摘要：methyl/alkyl chloroformate、Chirasil-L-Val、16 pairs段。
[13] Gas chromatographic analysis of amino acid enantiomers in Carbetocin peptide hydrolysates after fast derivatization with pentafluoropropyl chloroformate. (2008). DOI 10.1007/s00726-007-0577-1. GC：五氟丙基氯甲酸酯快速衍生化，结合手性柱GC/FID分析肽水解液。 核查层级：公开摘要与书目。证据位置：题名；摘要：traditional acid hydrolysis、GC/FID、Carbetocin段。
[14] GC separation of amino acid enantiomers via derivatization with heptafluorobutyl chloroformate and Chirasil-L-Val column. (2009). DOI 10.1002/jssc.200900400. GC：七氟丁基氯甲酸酯（HFBCF）衍生化后，在Chirasil-Val柱评价氨基酸对映体分离。 核查层级：公开摘要与书目。证据位置：摘要：HFBCF、19 AA enantiomers、except proline/arginine/cystine段。
[15] Enantioseparation of chiral amino acids as the N(O,S)-ethoxycarbonylated diastereomeric esters by achiral dual-capillary column gas chromatography. (2001). DOI 10.1039/b106610m. GC：氯甲酸乙酯引入EOC保护，再用(S)-(+)-3-甲基-2-丁醇等手性醇酯化；在非手性DB-5/DB-17柱拆分非对映异构体。 核查层级：公开摘要与书目。证据位置：摘要：ethyl chloroformate、chiral alcohol、achiral columns及Yakult段。
[16] Analysis of amino acid enantiomers derived from antitumor antibiotics using chiral capillary electrophoresis. (1997). DOI 10.1016/s0731-7085(97)00020-4. CE：FITC和Dansyl-Cl。文中分别用于LIF及UV检测，结合金属螯合CE和环糊精MEKC分析抗肿瘤缩肽完全水解液。 核查层级：公开摘要与书目。证据位置：摘要中hydrolysate、dansyl chloride、fluorescein isothiocyanate及应用段。
[17] Cyclodextrin-Modified Capillary Zone Electrophoresis for the Chiral Analysis of Proline and Hydroxyproline Stereoisomers in Chicken Collagen Hydrolysates. (2025). DOI 10.3390/ijms26125832. CZE：(R)-NCS为手性异硫氰酸酯；结合β-CD/DM-β-CD分离Pro及羟脯氨酸异构体。OPA/ME在本法中是预封闭伯胺步骤，不是目标仲胺的主标记试剂。 核查层级：全文＋摘要。证据位置：已读全文：2.1、2.2、2.3；3.1、3.3、3.4；Figures 2、5、6。
[18] Chiral separation and determination of excitatory amino acids in brain samples by CE-LIF using dual cyclodextrin system. (2012). DOI 10.1007/s00216-012-6384-x. CE：NBD-F标记Asp/Glu；双环糊精CE-LIF分离并测定脑样品中的对映体。 核查层级：公开摘要与书目。证据位置：摘要：fluorescent derivatization with 4-fluoro-7-nitro…及brain samples段。
[19] CE-LIF chiral separation of aspartic acid and glutamic acid enantiomers using human serum albumin and sodium cholate as dual selectors. (2009). DOI 10.1002/jssc.200900341. CE：DTAF标记Asp/Glu，HSA/胆酸钠双选择剂辅助对映体分离。DTAF属于芳香亲核取代标记，不是异硫氰酸酯。 核查层级：公开摘要与书目。证据位置：摘要：DTAF全名、HSA and SC、compound amino acids injection段。
[20] Method for on-line derivatization and separation of aspartic acid enantiomer in pharmaceuticals application by the coupling of flow injection with micellar electrokinetic chromatography. (2005). DOI 10.1016/j.chroma.2005.03.019. MEKC：OPA＋2-巯基乙醇（ME）标记，β-CD提供手性识别，SDS提供胶束体系。 核查层级：公开摘要与书目。证据位置：摘要：derivatization reagents、chiral selector、micellar chemical及real sample段。
[21] Separation and enantiomer determination ofOPA-derivatised amino acids by using capillary zone electrophoresis. (1992). DOI 10.1007/bf00806080. CE：OPA＋手性硫醇生成非对映异构体；文中研究自由溶液CE和SDS-MECC。 核查层级：公开摘要与书目。证据位置：摘要首句及MECC/free solution段。
[22] 3-[(3-Dehydroabietamidopropyl)dimethylammonio]-1-propane-sulfonate as a new type of chiral surfactant for enantiomer separation in micellar electrokinetic chromatography. (2007). DOI 10.1016/j.chroma.2007.01.139. MEKC：NDA标记氨基酸，DHAMAP手性表面活性剂提供手性分离。 核查层级：公开摘要与书目。证据位置：摘要：NDA-D/L-amino acids、chiral surfactant及6 pairs段。
[23] Chiral capillary electrophoresis with UV-excited fluorescence detection for the enantioselective analysis of 9-fluorenylmethoxycarbonyl-derivatized amino acids. (2018). DOI 10.1007/s00216-018-1148-x. CE：FMOC-Cl；β-CD辅助手性分离，并用UV激发荧光检测，应用于脑脊液。 核查层级：全文＋摘要。证据位置：已读全文：Introduction、Chemicals、AA derivatization、Results and discussion/CSF application。
[24] Enantiomeric separation of amino acids using micellar electrokinetic chromatography after pre-column derivatization with the chiral reagent 1-(9-fluorenyl)-ethyl chloroformate. (1995). DOI 10.1002/elps.1150160183. MEKC：手性FLEC衍生化后用SDS体系分离非对映异构体；同时比较FMOC＋环糊精的直接分离路线。 核查层级：公开摘要与书目。证据位置：摘要：(+)-/(-)-FLEC、SDS、diastereomers及FMOC比较段。
[25] Determination of sequence and absolute configuration of peptide amino acids by HPLC-MS/CD-based detection of liberated N-terminus phenylthiohydantoin amino acids. (2022). DOI 10.1038/s41598-022-14205-x. HPLC–MS/CD：PITC经Edman路线生成PTH-AA，建立对照并用于合成肽和天然缩肽；另分析合成肽酸水解液。 核查层级：全文＋摘要。证据位置：已读全文：Introduction、Results and discussion、Methods；摘要末句acid hydrolysates。
[26] High-throughput comprehensive analysis of D- and L-amino acids using ultra-high performance liquid chromatography with a circular dichroism (CD) detector and its application to food samples. (2011). DOI 10.1016/j.jchromb.2011.07.025. UHPLC–CD：筛选后选择NBD-F，利用g-factor计算%D，无需在柱上拆分同种氨基酸D/L。 核查层级：公开摘要与书目。证据位置：摘要：NBD-F was selected；does not require separation；food samples段。
[34] Enantioselective separation of amino acids as biomarkers indicating life in extraterrestrial environments. (2013). DOI 10.1007/s00216-013-6915-0. GC删除项审查：综述区分普通GC挥发化和对映体测定；常用MTBSTFA硅烷化被明确指出不适于其讨论的homochirality检测。不能把所有硅烷化剂概括为成熟手性氨基酸方案。 核查层级：公开摘要与书目。证据位置：摘要中silylation reagent…unsuitable for detection of homochirality段。
[35] Comparison of derivatization and chromatographic methods for GC-MS analysis of amino acid enantiomers in physiological samples. (2010). DOI 10.1016/j.jchromb.2010.03.021. GC限制性证据：比较氟化/非氟化酸酐及氯甲酸酯；PFPA/七氟丁醇虽灵敏，但衍生化消旋妨碍准确对映体定量，MCF路线可避免其问题。 核查层级：公开摘要与书目。证据位置：摘要：racemization during derivatization precluded accurate quantification及MCF段。
连接线机制标签核查（文献编号沿用上一版按出现顺序排序）：
HPLC：①手性固定相有[01]FITC＋万古霉素固定相支持，DOI 10.1016/j.foodchem.2007.11.062；②手性衍生化有[02]FDAA/GITC/OPA-IBLC＋反相HPLC支持，DOI 10.1016/j.chroma.2004.02.068，也有[03]Marfey证据。两路线为平台层面概括，不表示右侧每种试剂都适配两种路线。
GC：①手性固定相有[12]MCF＋Chirasil-L-Val支持，DOI 10.1016/j.chroma.2006.12.033；②手性衍生化有[15]ECF＋手性醇＋非手性DB-5/DB-17支持，DOI 10.1039/b106610m。
CE：不能将现有CZE/MEKC路线称为手性固定相。①手性选择剂有[16]金属螯合/环糊精CE-MEKC支持，DOI 10.1016/S0731-7085(97)00020-4；②手性衍生化有[21]OPA＋手性硫醇支持，DOI 10.1007/BF00806080；[24]FLEC＋SDS-MEKC支持，DOI 10.1002/elps.1150160183。手性选择剂与手性衍生化可合用，例如[17](R)-NCS＋DM-beta-CD，不是互斥条件。毛细管电色谱等可固定化选择剂的其他模式不由这里的CZE/MEKC文献自动证明。
HPLC-CD：现有[25]PITC-PTH文献（DOI 10.1038/s41598-022-14205-x）和[26]NBD-F文献（DOI 10.1016/j.jchromb.2011.07.025）均支持非手性衍生化/反相分离＋CD手性响应。它们不能证明本图所列方法采用了手性固定相或手性衍生试剂；因此该行线上方标为非手性衍生化，下方标为CD、UV、MS检测，不是两个并列手性分离备选策略。不据此断言其他HPLC-CD组合不存在。
版式：基于用户上传的13.333×7.5英寸版本；原有字号和方块大小保留，新增线上的策略标签18pt、线下检测标签16pt。
检测方式核查：HPLC列UV（原[02]明确UV/ESI-MS）、荧光（补充D1：10.1016/j.jchromb.2006.07.022，题名Determination of d-serine and related neuroactive amino acids in human plasma by high-performance liquid chromatography with fluorimetric detection，摘要明确OPA/IBLC＋HPLC荧光检测）、MS/MS（原[11]AQC/2D-LC-MS/MS）。GC列FID（原[13]卡贝缩宫素水解液论文明确GC/FID）与MS（原[12]GC-MS），不泛列未明确的MS/MS。CE列UV及荧光（原[16]分别对Dansyl和FITC采用UV/LIF；原[17]为LEDIF）与MS（补充D2：10.1002/elps.201600015，Enantioselective analysis of proteinogenic amino acids in cerebrospinal fluid by capillary electrophoresis-mass spectrometry，摘要明确FMOC/β-CD/CE-MS）。HPLC-CD列CD与UV（原[26]NBD-F）以及MS（原[25]PTH/HPLC-MS-CD）。图中荧光是FLD/LIF/LEDIF的上位简称，不意味着各平台共用同一荧光检测器。检测方式为文献中的代表例，不能推定每种试剂均适配所列全部检测器；未因仪器理论兼容性自行补入DAD、CAD等。
2026-10-28补充核查：原文献25/26仅覆盖非手性衍生化，不能据此限制整个HPLC-CD平台。新增[27]明确用CROWNPAK CR(+)拆分未衍生化D/L-Trp，并用CD-1595在233nm在线检测；Figure4给出相反CD峰。DOI 10.3390/ijms10062578。其对象为标准品和酶反应液，不是蛋白水解液。[28]采用非手性HSS T3直接分离未衍生化Phe并在线CD测猪胰岛素水解液；同文CROWNPAK手性柱只用于D-Phe光学纯度检查，不能把两步混同。DOI 10.1038/s41598-018-25682-4。因此上方两种路线改为手性固定相/非手性分离，下方列CD、UV、MS。样品可未衍生化，也可经文献支持的非手性衍生化；该图不据此增加手性衍生化＋CD支线，不把Trp响应外推到Leu/Lys等。新34/35为原删除项限制性来源，见配套全文献表。

## Slide 2
选择原则：文献初筛 → 三条候选思路 → 实验复筛
已有分析方法与衍生化试剂
文献初筛
1 选择HPLC–CD
UV/CD信息互补 [26]
不拆分D/L求比例 [26]
特定AA直测 [27,28]
2 筛选衍生化试剂
非手性≠不会消旋
UV/CD响应须实测
兼顾效率与稳定性
三条候选思路
拟用HPLC–UV/CD评价
PITC
现有方法作基线 [29]
PTC的CD待验证
AQC
稳定脲衍生物 [30]
pH/CD需确认
OPA＋非手性硫醇
快速、易自动化 [31]
稳定性依条件 [32]
实验复筛思路
1 实际样品适用
峰归属与UV/CD信号
稳定性/回收/精密度
水解与衍生构型保持
Phe、Leu、Lys
2 D/L定量关系
固定总浓度混配D/L
一起衍生，测CD/UV
拟合响应比—ee曲线
浓度挑战＋独立质控
方法图已补：手性柱与未衍生化直接分析
拟利用的优势：非手性标签＋UV/CD联合信息
不必拆分D/L即可校准比例 [26]；D/L可呈相反CD响应 [25]
上述CD优势来自NBD-F/PTH文献，不代表三候选已验证。ee详细方案见第3页；三法差异见第4页。
Notes: 本页依据用户第二页的左图/大括号/文献初筛/三个候选/实验复筛布局重整。文献初筛并非排除所有无现成CD文献的研究候选，而是将“已有UV/反应依据”与“待验证CD假设”区分。将原文“非手性试剂不会导致消旋”修正：非手性只表示不另引固定手性中心，消旋必须考察。已有手性柱/原生CD路线[27,28]并入左图，平台不再被描述为仅可非手性衍生化。PITC是原有PTC基线，不能沿用PTH的CD判断；AQC稳定脲和直接进样依据[30]；OPA快速/自动化依据[31]，稳定性需条件化[32]。三个方案的CD信号强弱/稳定性排名尚无本课题实测对比，不预设最优者。EE简要方案为拟议设计：固定总摩尔浓度、先混D/L后一起衍生、带符号CD/UV峰面积比拟合ee、独立质控/浓度挑战。UV/CD互补与不拆分比例思路参考[26]，镜像响应参考[25]，不是各候选的既定能力。
参考文献：
[06] High-performance liquid chromatography evaluation of the enantiomeric purity of amino acids by means of automated precolumn derivatization with ortho-phthalaldehyde and chiral thiols.. DOI 10.1002/chir.22660. 核查：公开摘要与书目；摘要：N-acetyl-L-cysteine、N-isobutyryl-L-cysteine、PFP column段
[11] Comprehensive Online Reversed-Phase × Chiral Two-Dimensional Liquid Chromatography-Mass Spectrometry with Data-Independent Sequential Window Acquisition of All Theoretical Fragment-Ion Spectra-Acquisition for Untargeted Enantioselective Amino Acid Analysis.. DOI 10.1021/acs.analchem.2c03042. 核查：公开摘要与书目；摘要：AQC、chiral tandem column、two peptide hydrolysate samples及oxytocin段
[17] Cyclodextrin-Modified Capillary Zone Electrophoresis for the Chiral Analysis of Proline and Hydroxyproline Stereoisomers in Chicken Collagen Hydrolysates.. DOI 10.3390/ijms26125832. 核查：全文＋摘要；已读全文：2.1、2.2、2.3；3.1、3.3、3.4；Figures 2、5、6
[25] Determination of sequence and absolute configuration of peptide amino acids by HPLC-MS/CD-based detection of liberated N-terminus phenylthiohydantoin amino acids.. DOI 10.1038/s41598-022-14205-x. 核查：全文＋摘要；已读全文：Introduction、Results and discussion、Methods；摘要末句acid hydrolysates
[26] High-throughput comprehensive analysis of D- and L-amino acids using ultra-high performance liquid chromatography with a circular dichroism (CD) detector and its application to food samples.. DOI 10.1016/j.jchromb.2011.07.025. 核查：公开摘要与书目；摘要：NBD-F was selected；does not require separation；food samples段
[27] Tryptophanase-catalyzed L-tryptophan synthesis from D-serine in the presence of diammonium hydrogen phosphate.. DOI 10.3390/ijms10062578. 核查：全文＋摘要；全文：Results/Determination of optical isomeric form by circular dichroism；Figure 4；Experimental/Tryptophan analyses by use of HPLC。
[28] A novel potential primary method for quantification of enantiomers by high performance liquid chromatography-circular dichroism.. DOI 10.1038/s41598-018-25682-4. 核查：全文＋摘要；全文：Instruments and reagents；Optimization of the HPLC separation conditions；Figure 3（独立手性纯度检查）；Figures 4F、5D（实际在线CD）；pINS应用。
[29] Rapid analysis of amino acids using pre-column derivatization.. DOI 10.1016/s0378-4347(00)85133-6. 核查：公开摘要与书目；公开摘要：phenylthiocarbamyl derivative、primary and secondary amino acids、protein hydrolyzates、UV detection。
[30] Synthesis of a fluorescent derivatizing reagent, 6-aminoquinolyl-N-hydroxysuccinimidyl carbamate, and its application for the analysis of hydrolysate amino acids via high-performance liquid chromatography.. DOI 10.1006/abio.1993.1270. 核查：公开摘要与书目；公开摘要：stable unsymmetric urea、pH range 8.2–10.0、direct injection。
[31] Analysis of amino acid composition in proteins of animal tissues and foods as pre-column o-phthaldialdehyde derivatives by HPLC with fluorescence detection.. DOI 10.1016/j.jchromb.2014.03.025. 核查：公开摘要与书目；公开摘要：primary AA、2-mercaptoethanol/3-mercaptopropionic acid、rapid formation、easy automation。
[32] The stability of the o-phthalaldehyde/2-mercaptoethanol derivatives of amino acids: an investigation using high-pressure liquid chromatography with a precolumn derivatization technique.. DOI 10.1016/0003-2697(84)90522-0. 核查：公开摘要与书目；公开摘要：stable on the HPLC column、optimal conditions。
[33] Comparison of different derivatisation for amino acids determination of foie gras by high performance liquid chromatography (HPLC).. DOI 10.1080/00071668.2024.2375723. 核查：公开摘要与书目；公开摘要：三种衍生化组、17种氨基酸、运行时间及与自动氨基酸分析仪比较。

## Slide 3
ee校准思路：固定总浓度，建立响应比—ee关系
适用于非手性LC上同一氨基酸的D/L共洗脱；手性柱分离时，应分别校准D、L峰。
eeD = (cD − cL) / (cD + cL) × 100% （D为正；不代表CD峰一定为正）
① 按物质的量配制9个比例水平
D:L摩尔比
理论eeD
100:0
+100%
90:10
+80%
75:25
+50%
60:40
+20%
50:50
0%
40:60
−20%
25:75
−50%
10:90
−80%
0:100
−100%
CT = cD＋cL保持恒定，浓度由预实验选定。
先按纯度、盐型校正，再混合并一起衍生。
② 取带符号响应比，再检验线性模型
R = SCD / SUV；拟合 R = a·eeD＋b
S为峰面积；CD面积保留正负号，校正空白、基线与通道时延。
R是经验响应比，不直接等于g因子；每个氨基酸单独校准。
③ 用独立样品验证，不只看校准点或R²
独立配制±40%、±70%等QC；固定ee改变CT，检查浓度依赖。
高ee端加密；需要微量对映体结论时用手性LC复核。
设置经/不经水解的对照，并用已知构型肽排查水解与衍生偏差。
建议每点≥3份独立制备；先确认目标峰/产物与响应线性，再预设回算偏差和精密度接受标准。
依据[25–26]提出的实验方案，尚未执行；9点、QC与重复数为本项目建议，不是原文照录。
Notes: 本页明确为尚未实施的实验设计，不包含测定数据或虚构回归系数。CT固定、已校正纯度/盐型的D/L标液按物质的量配比后统一衍生，避免仅事后混合衍生物掩盖反应选择性。eeD百分数范围-100至+100，R=a eeD+b中的ee单位始终用百分数；未知样品eeD=(R-b)/a。S_CD必须是带符号峰面积，不可取绝对值；S_UV反映同一目标衍生物总量，不能混入其他共洗脱组分。若两个检测器串联，校正流路时延并一致积分，CD和UV检测波长/增益固定。经验R不是未经单位/光程换算的无量纲g。每种氨基酸、试剂、产物和条件独立建模；先检验D/L镜像、外消旋抵消、相同反应效率及无消旋，检查残差/失拟，不应仅以高R²接受。Lys多位点产物先确认单/双衍生物身份与定量峰。独立QC与浓度挑战用于证实模型可转移。高ee的少量反对映体不能仅凭相减法认为达到痕量定量能力，须与手性分离正交验证。UV/CD低于适用定量/信噪范围时不报告可靠ee。水解对照的游离氨基酸不能完全替代已知构型肽的真实释放/消旋过程，因此两类对照互补。文献25证明标准PTH响应及水解液应用，文献26证明NBD-F/CD-g因子比例方法；本页具体水平和QC为研究建议，并非对PTC/AQC/OPA既定线性性能的承诺。
参考文献：
[06] High-performance liquid chromatography evaluation of the enantiomeric purity of amino acids by means of automated precolumn derivatization with ortho-phthalaldehyde and chiral thiols.. DOI 10.1002/chir.22660. 核查：公开摘要与书目；摘要：N-acetyl-L-cysteine、N-isobutyryl-L-cysteine、PFP column段
[11] Comprehensive Online Reversed-Phase × Chiral Two-Dimensional Liquid Chromatography-Mass Spectrometry with Data-Independent Sequential Window Acquisition of All Theoretical Fragment-Ion Spectra-Acquisition for Untargeted Enantioselective Amino Acid Analysis.. DOI 10.1021/acs.analchem.2c03042. 核查：公开摘要与书目；摘要：AQC、chiral tandem column、two peptide hydrolysate samples及oxytocin段
[17] Cyclodextrin-Modified Capillary Zone Electrophoresis for the Chiral Analysis of Proline and Hydroxyproline Stereoisomers in Chicken Collagen Hydrolysates.. DOI 10.3390/ijms26125832. 核查：全文＋摘要；已读全文：2.1、2.2、2.3；3.1、3.3、3.4；Figures 2、5、6
[25] Determination of sequence and absolute configuration of peptide amino acids by HPLC-MS/CD-based detection of liberated N-terminus phenylthiohydantoin amino acids.. DOI 10.1038/s41598-022-14205-x. 核查：全文＋摘要；已读全文：Introduction、Results and discussion、Methods；摘要末句acid hydrolysates
[26] High-throughput comprehensive analysis of D- and L-amino acids using ultra-high performance liquid chromatography with a circular dichroism (CD) detector and its application to food samples.. DOI 10.1016/j.jchromb.2011.07.025. 核查：公开摘要与书目；摘要：NBD-F was selected；does not require separation；food samples段
[27] Tryptophanase-catalyzed L-tryptophan synthesis from D-serine in the presence of diammonium hydrogen phosphate.. DOI 10.3390/ijms10062578. 核查：全文＋摘要；全文：Results/Determination of optical isomeric form by circular dichroism；Figure 4；Experimental/Tryptophan analyses by use of HPLC。
[28] A novel potential primary method for quantification of enantiomers by high performance liquid chromatography-circular dichroism.. DOI 10.1038/s41598-018-25682-4. 核查：全文＋摘要；全文：Instruments and reagents；Optimization of the HPLC separation conditions；Figure 3（独立手性纯度检查）；Figures 4F、5D（实际在线CD）；pINS应用。
[29] Rapid analysis of amino acids using pre-column derivatization.. DOI 10.1016/s0378-4347(00)85133-6. 核查：公开摘要与书目；公开摘要：phenylthiocarbamyl derivative、primary and secondary amino acids、protein hydrolyzates、UV detection。
[30] Synthesis of a fluorescent derivatizing reagent, 6-aminoquinolyl-N-hydroxysuccinimidyl carbamate, and its application for the analysis of hydrolysate amino acids via high-performance liquid chromatography.. DOI 10.1006/abio.1993.1270. 核查：公开摘要与书目；公开摘要：stable unsymmetric urea、pH range 8.2–10.0、direct injection。
[31] Analysis of amino acid composition in proteins of animal tissues and foods as pre-column o-phthaldialdehyde derivatives by HPLC with fluorescence detection.. DOI 10.1016/j.jchromb.2014.03.025. 核查：公开摘要与书目；公开摘要：primary AA、2-mercaptoethanol/3-mercaptopropionic acid、rapid formation、easy automation。
[32] The stability of the o-phthalaldehyde/2-mercaptoethanol derivatives of amino acids: an investigation using high-pressure liquid chromatography with a precolumn derivatization technique.. DOI 10.1016/0003-2697(84)90522-0. 核查：公开摘要与书目；公开摘要：stable on the HPLC column、optimal conditions。
[33] Comparison of different derivatisation for amino acids determination of foie gras by high performance liquid chromatography (HPLC).. DOI 10.1080/00071668.2024.2375723. 核查：公开摘要与书目；公开摘要：三种衍生化组、17种氨基酸、运行时间及与自动氨基酸分析仪比较。

## Slide 4
三条候选思路：比较的是实验分工，不是预设CD性能排名
PITC作已有方法基线，AQC作稳定标记参照，OPA作快速流程候选；最终由同一验证框架筛选。
比较维度
PITC（本项目PTC）
AQC
OPA＋非手性硫醇
产物与检测依据
PTC衍生物；蛋白水解物
UV分析 [29]
稳定非对称脲；水解物
荧光分析 [30]
异吲哚衍生物；蛋白组成
荧光分析 [31]
相对可取之处
衔接已有样品/色谱条件；便于形成方法基线
稳定标记，反应液可直接进样；便于评价等待进样影响 [30]
快速反应、易自动化；适合比较高效率流程 [31]
应付出的验证工作
确认PTC身份、副产物与回收；
不可套用PTH的CD结论
量测最终反应pH；确认
反应完成后评价CD信噪比
硫醇与计时需锁定；
稳定性依具体条件 [32]
当前CD证据边界
有PTH-CD文献 [25]；
不等同PTC-CD
有AQC手性LC证据 [11]；
不等同CD证据
常规HPLC/FLD证据 [31]；
不等同在线CD证据
本项目研究定位
现有方法基线
稳定定量/批量分析参照
快速衍生化候选
[33]比较的是特定基质中的OPA–FMOC/PITC/AQC组成分析；不能外推为OPA单独体系或CD的优劣排名。
Notes: 比较只涉及文献支持的反应/产物/流程特点及本项目的研究分工。PITC经典文献29指出快速、高效地形成PTC并用于蛋白水解物伯/仲胺UV分析，不能将用户某个1h反应/萃取方案视为PITC方法固有地慢。AQC文献30明确稳定非对称脲、快速一步反应、直接进样、pH和试剂过量影响收率；这不证明AQC在本项目CD信号最强。OPA文献31总结快速反应、自动化、非手性硫醇荧光应用；文献32指出特定OPA/ME产物柱上稳定，因此不能泛称所有OPA产物均极不稳定。等待进样稳定性需按实际硫醇/目标AA/pH测定。原文献6在手性硫醇OPA体系指出产品稳定性问题及在线衍生改善，只能作特定体系补充，不与非手性体系混同。文献33的OPA-FMOC组合、不同运行时间/基质结果不是本课题三候选直接在线CD比较。主张是互补对照，不给出没有同平台数据支持的灵敏度、成本、回收或CD排名。
参考文献：
[06] High-performance liquid chromatography evaluation of the enantiomeric purity of amino acids by means of automated precolumn derivatization with ortho-phthalaldehyde and chiral thiols.. DOI 10.1002/chir.22660. 核查：公开摘要与书目；摘要：N-acetyl-L-cysteine、N-isobutyryl-L-cysteine、PFP column段
[11] Comprehensive Online Reversed-Phase × Chiral Two-Dimensional Liquid Chromatography-Mass Spectrometry with Data-Independent Sequential Window Acquisition of All Theoretical Fragment-Ion Spectra-Acquisition for Untargeted Enantioselective Amino Acid Analysis.. DOI 10.1021/acs.analchem.2c03042. 核查：公开摘要与书目；摘要：AQC、chiral tandem column、two peptide hydrolysate samples及oxytocin段
[17] Cyclodextrin-Modified Capillary Zone Electrophoresis for the Chiral Analysis of Proline and Hydroxyproline Stereoisomers in Chicken Collagen Hydrolysates.. DOI 10.3390/ijms26125832. 核查：全文＋摘要；已读全文：2.1、2.2、2.3；3.1、3.3、3.4；Figures 2、5、6
[25] Determination of sequence and absolute configuration of peptide amino acids by HPLC-MS/CD-based detection of liberated N-terminus phenylthiohydantoin amino acids.. DOI 10.1038/s41598-022-14205-x. 核查：全文＋摘要；已读全文：Introduction、Results and discussion、Methods；摘要末句acid hydrolysates
[26] High-throughput comprehensive analysis of D- and L-amino acids using ultra-high performance liquid chromatography with a circular dichroism (CD) detector and its application to food samples.. DOI 10.1016/j.jchromb.2011.07.025. 核查：公开摘要与书目；摘要：NBD-F was selected；does not require separation；food samples段
[27] Tryptophanase-catalyzed L-tryptophan synthesis from D-serine in the presence of diammonium hydrogen phosphate.. DOI 10.3390/ijms10062578. 核查：全文＋摘要；全文：Results/Determination of optical isomeric form by circular dichroism；Figure 4；Experimental/Tryptophan analyses by use of HPLC。
[28] A novel potential primary method for quantification of enantiomers by high performance liquid chromatography-circular dichroism.. DOI 10.1038/s41598-018-25682-4. 核查：全文＋摘要；全文：Instruments and reagents；Optimization of the HPLC separation conditions；Figure 3（独立手性纯度检查）；Figures 4F、5D（实际在线CD）；pINS应用。
[29] Rapid analysis of amino acids using pre-column derivatization.. DOI 10.1016/s0378-4347(00)85133-6. 核查：公开摘要与书目；公开摘要：phenylthiocarbamyl derivative、primary and secondary amino acids、protein hydrolyzates、UV detection。
[30] Synthesis of a fluorescent derivatizing reagent, 6-aminoquinolyl-N-hydroxysuccinimidyl carbamate, and its application for the analysis of hydrolysate amino acids via high-performance liquid chromatography.. DOI 10.1006/abio.1993.1270. 核查：公开摘要与书目；公开摘要：stable unsymmetric urea、pH range 8.2–10.0、direct injection。
[31] Analysis of amino acid composition in proteins of animal tissues and foods as pre-column o-phthaldialdehyde derivatives by HPLC with fluorescence detection.. DOI 10.1016/j.jchromb.2014.03.025. 核查：公开摘要与书目；公开摘要：primary AA、2-mercaptoethanol/3-mercaptopropionic acid、rapid formation、easy automation。
[32] The stability of the o-phthalaldehyde/2-mercaptoethanol derivatives of amino acids: an investigation using high-pressure liquid chromatography with a precolumn derivatization technique.. DOI 10.1016/0003-2697(84)90522-0. 核查：公开摘要与书目；公开摘要：stable on the HPLC column、optimal conditions。
[33] Comparison of different derivatisation for amino acids determination of foie gras by high performance liquid chromatography (HPLC).. DOI 10.1080/00071668.2024.2375723. 核查：公开摘要与书目；公开摘要：三种衍生化组、17种氨基酸、运行时间及与自动氨基酸分析仪比较。